....	....	Antifreeze heating for siphons (FSH-S)

Antifreeze heating for the use in all common suction and

pressure side type siphons with 1½" connection.

In general the antifreeze heating consists of a flexible heating cable

which is led through the siphon and energized automatically by a

variably adjustable thermostat as soon as the set temperature is

fallen below.

Heating the cable prevents the siphon from freezing.

Technical data:

Voltage: 230 V, heated length: 70cm, self-regulating heating cable,

power: 19W/m (at 10°C) and 30W/m (at -25°C), heating power:

13.3W (at 10°C) and 21W at (-25°C), protection class I, model with

protective conductor, completely watertight in the heated area from

connecting sleeve.

Supply cable, unheated, 100cm, in IP54,

Admissible operating temperature -30°C to +55°C

- For universal use in all 1½" siphons

- Easy retrofit

- Preassembled

- Including connection box (IP67) with integrated antifreeze
thermostat for installation in the immediate environment 
of the siphon

- Completely equipped with clamps for an easy connection to 
the existing electrical supply (3 x 1.5 mm²), 230V UPS required

- Thermostat preset to +5° C

Delivery

Type		:	FSH-S

Make		:	Klima-Komponenten-Küch GmbH

Tel.: 	+49 (0) 2238-922660

Fax: 	+49 (0) 2238-140807

Email: 	info@klima-kuech.com

....	....	As above, but

Antifreeze heating for siphons (FSH-D)

with T-piece

Delivery

Type		:	FSH-D

Make		:	Klima-Komponenten-Küch GmbH

Tel.: 	+49 (0) 2238-922660

Fax: 	+49 (0) 2238-140807

Email: 	info@klima-kuech.com