....	....	Special siphon – Pressure side type AK-D (white)

Special siphon for draining condensate from the chiller, humidifier 
or other wet areas in air-handling (AH) units that operate at 
positive pressure compared to the environment.

Individual outlet construction and variable installation height.

End cap for filling and inspection purposes.

Suitable for a max. positive pressure of P = 1,690 Pa considering 
a safety factor of 1.5 for pressure fluctuations in the system.

Made of polypropylene (PP).

Water intake connection via crimp screwing or rubber sleeve for 
outlets of ¾“, 1“, 1¼“, 1½“.

Outlet diameter 40 mm.

Delivery

Type		:	AK-D

Make	:	Klima-Komponenten-Küch GmbH

Tel.: 	+49 (0) 2238-922660

Fax: 	+49 (0) 2238-140807

Email: 	info@klima-kuech.com

....	....	As above, but

Special siphon – Pressure side type AK-D-T (transparent)

Delivery

Type		:	AK-D-T

Make		:	Klima-Komponenten-Küch GmbH

Tel.: 	+49 (0) 2238-922660

Fax: 	+49 (0) 2238-140807

Email: 	info@klima-kuech.com